## Slide 1: dMOdels – graphical user interface (GUI)
Maurizio Battaglia & Thy Do

## Slide 2: Overview
I. Environment set up
II. Available functions
III. I/O Files handling
IV. Further assistance

## Slide 3: I) Environment set up
1) Java platform
Latest Java environment installed on the device. (Java 8)
Java and dMODELS are not supported on mobile device.
Details on how to download and install a Java platform compatible with your device system can be found via this link: https://www.java.com/en/download/help/index_installing.xml
2) MATLAB MCR
Latest MATLAB Runtime installed on the device. (MATLAB MCR R2017a)
Details on how to install and update can be found here: https://www.mathworks.com/products/compiler/mcr.html

## Slide 4: II) functions
1) Utilities
2) Running the inversion
- Choose data
- Choose source
- Input parameters
- Edit data file

## Slide 6: Utilities overview
LL-UTM Conversion
Create KML
Pre Processing

## Slide 7: LL-UTM Conversion
Utilities -> UTM_LL Conversion
2 ways to input data:
  File -> Open -> .txt file
    File name should be strictly either
    UTMfile.txt or LLfile.txt.
  Manually input
  -Enter number of sites.
  -Fill in either one of the table with relevant data.
Click Convert to start the process.

## Slide 8: LL-UTM Conversion
Save file:
Click File -> Save File: UTM file or LL file.
Reset table:
      Click Edit -> Reset: clear all data available in both UTM and LL table.

## Slide 9: Create KML
Prerequisite:
Geodetic data file
Note coordinates in Lat, Long
- Only file name, whether you want to plot contour map and the vector plot scale factor are important.

## Slide 10: Create KML
Click Utilities -> Create KML. Wait for the application to process.
There are 2 types of output files. You will be prompted whether to save the result files. Click Yes to Save and No to proceed.
File name: [Volcano][Year].kml

## Slide 11: Pre-Processing
Prerequisite:
Geodetic data file
Note coordinates in X, Y
- Only file name, whether to plot contour map and scale factor are important
Click Utilities -> Pre Processing to run the application

## Slide 12: Running the inversion
Y/N choice:
-Plot contour map
-Best fit solution
-Error computation
-Model data with
vertical spheroid
(only spheroid source)

## Slide 13: Running the inversion
In order to run the inversion code, you want to make sure these filled out:
Your geodetic data choice
Your source choice
Your Data tab with all parameters and data accordingly to your chosen source and geodetic data. (N/A for all blank space)
After all data and parameters filled in, click Run Inversion to proceed and receive the results

## Slide 14: Running the inversion
If “Plot contour map” field is the map.txt file to proceed the inversion. indicated “Y”, you will need to import.
A logo will pop up indicating that the application is running, you should wait for a moment for the results to be displayed.

## Slide 15: III) I/O files handling
How to input parameters?
There are 2 ways to input your parameters.
1) Import file (.txt):
* a parameter file that is strictly named “InputDataFile”.
*File -> Open -> Folder of file -> InputDataFile.txt
2) Manually import
*Make sure to put N/A to all the fields that are not applicable to your chosen type of geodetic data and source.

## Slide 16: Inputdatafile.txt
Sphere and Sill
Dislocation

## Slide 17: Inputdatafile.txt
Spheroid

## Slide 18: III) I/O files handling
B) How to input data?
There are 2 ways to import your data to the table.
1) Import the data file (.txt): a data file that is named with your project (ex: Augustine2006)
File -> Open -> Folder of file -> ProjectName.txt
Suggested name: [Volcano][Year].txt
2) Manually import the data from each site through the column on the right and click Add.

## Slide 19: [Volcano][year].txt

## Slide 20: III) I/O files handling
C) How to modify the data in the table?
*Delete: Choose the row where you want to delete, click Delete.
This will remove the whole data of the chosen site.

## Slide 21: III) I/O files handling
*Update: Choose the row you want to update the data.
Fill in the new adjustment to the column on the right and click Update.
This will adjust your chosen row accordingly to the data filled in the column.

## Slide 22: III) I/O files handling
D) How to save output files?
There are 2 types of output files:
1).jpeg (represented by separated windows)
To save the image file as .jpeg, click File -> Save in each image window.

## Slide 23: III) I/O files handling

## Slide 24: III) I/O files handling
2).txt (represented by tabs)
To save file as .txt, click on the tab you want to save, click File -> Save Current Tab -> Yes

## Slide 25: III) I/O files handling

## Slide 26: iV) Further assistance
*For further guidance on using the application, click Help.
*Should you encounter any problems or find any bugs, please contact doth01@gettysburg.edu